## Slide 1: Kalyani Government Engineering College IoT based Unmanned Aerial Vehicle for Surveillance using Wireless Sensor Network
Presented by
Shubham Khan
Under guidance of
Prof. Swapan Kumar Mondal
Final Year Postgraduate 2019-21
University Roll no : 10211219006
KGEC/CSE/MTECH/2nd YEAR
Page: i

## Slide 2: Outline
Overview
Components Required
UAV Implementation
  Hardware Implementation
  Flight controller configuration
  Developed object detection
Result
Test Flight
Discussion
Conclusion
Future work
References
Page: ii
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 3: Overview
Page: 1
Outline
In simple words, this project is an unmanned aerial vehicle used for surveillance and it is remotely controlled by using a transmitter and receiver. It can also be used for human detection.
Where do we need this project?
Search and rescue.
Military application.
Product delivery.
News reporting.
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 4: Components Required
Page: 2
Outline
Fig 1: Project Components
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 5: UAV Implementation
Hardware Implementation
Flight controller configuration
Developed object detection
Page: 3
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 6: Hardware Implementation: Overview
Page: 4
Outline
Fig 2: Working Principle
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 7: Hardware Implementation: Assembly
Fig 3: UAV Assembly
Page: 5
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 8: Hardware Implementation: UAVs action
Page: 6
Outline
Fig 4: Type of UAVs action
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Roll: This helps move the UAV in the air to the left or right.
Pitch: This helps the UAV to move forward or backward.
Yaw: This helps the UAV to rotate clockwise or counterclockwise.
Throttle: This helps the UAV to move faster or slower.

## Slide 9: Flight Controller Configuration
Firmware Installing
ESC Calibration
Compass Calibration
Accelerometer Calibration
Radio Control Calibration
Flight Mode Configuration
Page: 7
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 10: Firmware Installing
Fig 5: Firmware Installing
Page: 8
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 11: ESC Calibration
Fig 6: ESC Calibration
Page: 9
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 12: Compass Calibration
Fig 7: Compass Calibration
Page: 10
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 13: Accelerometer Calibration
Fig 8: Accelerometer Calibration
Page: 11
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 14: Radio Control Calibration
Fig 9: Radio Control Calibration
Page: 12
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 15: Flight Mode Configuration
Fig 10: Flight Mode Configuration
Page: 13
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 16: Object detection
Choosing a pre-training model
Preprocessing Images and Labels
Generating TF record
Training and Testing
Page: 14
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 17: Choosing a pre-training model
Fig 11: Basic architecture of CNN
Page: 15
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Convolutional Neural Network (CNN) is a Deep Learning algorithm which can take in an input image, assign importance to various objects in the image and be able to differentiate one from the other. Here we choos Single Shot Detector (SSD) MobileNet for object detection.

## Slide 18: Preprocessing Images and Labels
Fig 12: Images labeling
Page: 16
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Here we create an annotation file by using labelimg software use the bounding box technique to making rectangular boxes around similar objects.

## Slide 19: Generating TF record
Page: 17
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Tensorflow accepts data in the form of TFRecords, a binary file that runs quickly and uses little memory. Instead of loading the entire data set into memory, Tenorflow uses these TFRecords to automatically divide the data into chunks.

## Slide 20: Training and Testing
Fig 13: Tranning process
Page: 18
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Object detecation models train themselves in this technique.

## Slide 21: Result
Hardware result
Object detection result
Page: 19
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 22: Hardware result
Fig 14: Hardware result
Page: 20
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 23: Object detection result
Fig 15: Object detection result
Page: 21
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 24: Test Flight
Fig 16: Test Flight
Page: 22
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 25: Discussion
Table 2: Confusion matrix
Page: 23
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
When an object is present in the image and the model can detect the object, it is called True Positive (TP).
When an object is missing in the figure and the model can detect the object, it is called a False Positive (FP).
When an object is present in the figure but the model fails to identify the object, it is called False Negative (FN).
When an object is missing in the image and the model fails to identify the object, it is called True Negative (TN).
Image | 1.jpg | 2.jpg | 3.jpg | 4.jpg | 5.jpg | 6.jpg | 7.jpg | 8.jpg | 9.jpg | 10.jpg
Truth | People | People | No People | People | No People | People | People | People | No People | No People
Predict | People | No People | People | People | No People | People | People | People | People | No People
Table 1: Test image prediction
 |  | Actual | 
 |  | Positive | Negative
Predicted | Positive | TP = 5 | FP = 2
 | Negative | FN = 1 | TN = 2

## Slide 26: Discussion – contd.
Page: 24
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Here we get the accuracy of our model is 70%
Accuracy is used to evaluate classification models. Accuracy is the ability to verify that a fraction of predictions are correct for a model or not. Accuracy is not always selected as the best model.
The formula for accuracy is as follows:

## Slide 27: Discussion – contd.
Page: 25
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
The number of correct positive predictions made by the model is known as Precision. Following is the Precision formula:
Here we get the Precision of our model is 0.71

## Slide 28: Discussion – contd.
Page: 26
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
The number of correct positive predictions made out of all positive predictions made by the model is known as Recall. Following is the Recall formula:
Here we get the Recall of our model is 0.83

## Slide 29: Discussion – contd.
Page: 27
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
The other measure is the F1 Score which is a function of Precision and Recall. F1 Score is required when you balance between Precision and Recall. It is a better measure technic over Accuracy. Following is the F1 Score formula:
Here we get the F1 Score of our model is 0.76

## Slide 30: Conclusion
Page: 28
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
This project is based on surveillance. Here a UAV has been made suitable for surveillance of a specific area. We launched this project to monitor from the sky and use UAV surveillance for human detection. With a camera mounted on a UAV, we can capture video and use that video for surveillance.
This is how we decided to finish our project. However, this is not the end because I am very keen to work on this project, so I am willing to do some more work on this project if I get any next opportunity in the future.

## Slide 31: Future work
Page: 29
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021
Increasing UAV coverage diameter.
Enable 24-hour surveillance even at night.
Camera video footage compression without losing video quality.
UAVs flying in residential areas by generating less noise.
Maximum work with minimum power loss.
Developing UAV controlling software for the ground station.

## Slide 32: References
Aber, J.S., 2004. Lighter-than-air platforms for small-format aerial photography. Transactions of the Kansas Academy of Science, 107(1), pp.39-44.
SPEARMAN, M., 1978, January. Historical development of world wide guided missiles. In 16th Aerospace Sciences Meeting (p. 210).
Awange, J. and Kiema, J., 2019. Unmanned aircraft vehicles. In Environmental Geoinformatics (pp. 265-289). Springer, Cham.
Blom, J.D., 2010. Unmanned aerial systems: A historical perspective (Vol. 45). Kansas: Combat Studies Institute Press.
Zaloga, S.J., 2011. Unmanned aerial vehicles: robotic air warfare 1917–2007. Bloomsbury Publishing.
Kim, S.J., Jeong, Y., Park, S., Ryu, K. and Oh, G., 2018. A survey of drone use for entertainment and AVR (augmented and virtual reality). In Augmented Reality and Virtual Reality (pp. 339-352). Springer, Cham.
Chen, S., F Laefer, D. and Mangina, E., 2016. State of technology review of civilian UAVs. Recent Patents on Engineering, 10(3), pp.160-174.
Nakazawa, Anton, and Bai Xiang Jin. "Quadcopter Video Surveillance UAV." University of Victoria (2013).
Cox, T.H., Nagy, C.J., Skoog, M.A., Somers, I.A. and Warner, R., Civil UAV Capability Assessment.
Szczepański, C., 2015. UAVs and their avionic systems: development trends and their influence on Polish research and market. Aviation, 19(1), pp.49-57.
Fahlstrom, P. and Gleason, T., 2012. Introduction to UAV systems. John Wiley & Sons.
Page: 30
Outline
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021

## Slide 33: Ask me, if you have any questions?

## Slide 34: Thank you for your patience and support.

## Slide 35: Plagiarism statement
I check plagiarism from Introduction to conclusion. I used free software named duplichecker. This software can check plagiarism 1000 words at a time.
My report has a total of 8387 words. So I check it 9 times (912, 973, 931, 932, 965, 986, 966, 924, and 798). And results are coming (0, 0, 0, 0, 0, 0, 0, 4, and 4). So the final plagiarism number will be (4*0.924 + 4*0.798)/8.387= 0.821.
KGEC/CSE/MTECH/2nd YEAR
July 05th, 2021